## Slide 1
SILICON MINDS
One Student.
One Deadline.
One Chip.
How a solo engineer designed, verified, and optimized an FPGA CNN accelerator for the IEEE SSCS Egypt Chapter 2026 Student Design Competition
Basel | Team Silicon Minds | September 2026

## Slide 2
CHAPTER 1 — THE SPARK
Machines need to see. Most can't afford to.
Smart cameras, industrial inspection lines, and always-on sensors all want the same thing: recognize what they're looking at, instantly, on the device itself — no cloud, no delay, no big power bill.
That recognition starts with one operation, repeated millions of times a second: convolution — sliding a small kernel across an image and multiplying, adding, multiplying, adding.
Doing that on a general-purpose processor is slow and power-hungry. Doing it in dedicated silicon is the entire idea behind this project.
Edge vision
Cameras & sensors that must act on what they see, locally
Tight power budget
Battery- or PoE-powered devices, not a data-center rack
One core operation
N×N convolution — the heart of every CNN layer
IEEE SSCS Egypt Chapter 2026 Student Design Competition
02

## Slide 3
CHAPTER 2 — THE TURNING POINT
Then, weeks before the deadline, the team was gone.
Silicon Minds started as a team. By the time the real work began — architecture, RTL, verification, optimization, synthesis — it was one person and a deadline.
So the plan changed: not "finish what we started," but "own every stage, personally."
Architect
→
Code (RTL)
→
Verify
→
Optimize
→
Synthesize
Every result in this deck — every line of RTL, every test, every optimization — was built solo, start to finish.
03

## Slide 4
CHAPTER 3 — THE BLUEPRINT
Think of it as a factory line for pixels.
Instead of a general-purpose processor juggling instructions, the chip is a straight conveyor belt: the image goes in one end, and one finished answer comes out the other end — every single clock cycle.
Image Memory
Holds the picture, feeds it out
one pixel per tick
→
Line Buffer
Remembers the last few rows
so a full neighborhood exists
→
Window Slider
Frames the current N×N patch
of the image, live
→
Multiply-Add Engine
Blends the patch with the
kernel — the actual "thinking"
→
Output Stream
Optional clean-up (ReLU),
then streams the result out
Result: a fully pipelined design that produces one finished output pixel every clock cycle — no stalls once it gets going.
04

## Slide 5
CHAPTER 3 — THE BLUEPRINT
Nothing is hard-wired. Everything is a dial.
Any kernel, any time
The N×N kernel is loaded at runtime, coefficient by coefficient — swap edge-detection for something else without touching the chip design.
Any reasonable image size
32×32 is the floor, not the ceiling — verified running cleanly at 64×64 with no redesign.
ReLU on demand
A single control bit turns on activation clean-up — useful for vision, skippable when it's not.
Why it matters: the same chip design can be re-purposed for a different vision task just by reloading numbers — not re-spinning silicon.
05

## Slide 6
CHAPTER 4 — THE PROOF
A clever design that's wrong is worthless. So: prove it.
Before trusting a single result, every output the chip produces is checked, pixel by pixel, against an independent Python model computing the exact same math by hand.
Then a 46-case test plan pushes the design into every corner it could ever fail in: empty images, extreme values, resets mid-operation, back-to-back runs with zero gap, and invalid inputs on purpose.
A layered SystemVerilog testbench (its own small piece of software engineering) automates all of it, with coverage tracking to prove nothing was skipped.
900 / 900
output pixels bit-exact
against the golden model
46 test cases · 6 categories · full coverage plan
Functional · Boundary · Reset · Back-to-back · Error injection · Timing
06

## Slide 7
CHAPTER 5 — THE HUNT FOR EFFICIENCY
Working wasn't the finish line. Efficient was.
A correct first version quietly wasted resources: an output buffer sized for an entire image when only a handful of results are ever in flight at once — about 20,000 flip-flops doing almost nothing.
BEFORE
3.96 × 10⁻⁴
Figure of Merit · 100 MHz, unoptimized
7,396 LUTs · 0.339 W
An oversized output buffer built almost entirely from unnecessary flip-flops.
→
AFTER
7.52 × 10⁻³
Figure of Merit · 20 MHz, optimized
842 LUTs · 0.149 W
Right-sized buffer, a deliberate low-power clock choice, and a real reset-hazard fixed.
≈ 19× more efficient — with every decision traceable to a number, not a guess.
07

## Slide 8
CHAPTER 6 — THE NUMBERS
What the chip actually costs — and delivers.
842
LUTs used
1.6% of the Zynq-7020
0
DSP48 slices
kept at zero, on purpose
69.1 MHz
Max. frequency
20 MHz chosen for low power
0.149 W
Total power
estimated, fully routed
1 px/cyc
Throughput
fully pipelined, no stalls
7.52e-3
Figure of Merit
≈19× the unoptimized baseline
Fully routed implementation · Xilinx Zynq-7020 (xc7z020clg400-1), PYNQ-Z2
08

## Slide 9
CHAPTER 7 — WHY IT MATTERS
This isn't a classroom exercise. It's a building block.
The same pipeline that processes a 32×32 test image scales directly into the kind of always-on, battery-friendly vision the real world is short on: quality inspection on a production line, a security camera that decides locally, a sensor that doesn't need a data center to be useful.
And because the AXI4-Lite interface is already built in, this core drops straight into a Zynq system-on-chip — one register write away from being driven by a real ARM processor.
Bonus criteria met
One pixel / cycle, fully pipelined
Optional ReLU activation
AXI4-Lite, real-SoC ready
09

## Slide 10
CHAPTER 8 — LOOKING BACK
What solo actually taught.
1
A deadline doesn't care who's left on the team — only what's finished.
2
Every optimization needs a number behind it, or it's just a guess with extra steps.
3
Verification isn't the boring part after the design — it's what makes the design real.
10

## Slide 11
Built alone. Verified thoroughly.
Ready to be judged.
Silicon Minds · Basel
Full report, verification test plan, and SystemVerilog/QuestaSim environment available in the project repository.
Thank you.
11